## Slide 1
Gen2 Robusta ED (BUGA)
BEX for service lifts at high capacities
75 m / 24 stops
3000, 3500, 4000, 4500, 5000
40, 46, 53, 60, 66 passengers
0.5 / 0.8 / 1 / 1.6 /
1.75 m/s
Heavy freight elevators with proven Gen2 technology
Reasonable complement to
Gen2 Robusta
x

## Slide 2
Main characteristics overview
Gen2 Robusta ED
 |  |  | Duty Load & number of passengers |  |  |  | 
 |  |  | 3000 | 3500 | 4000 | 4500 | 5000
 |  |  | 40 | 46 | 53 | 60 | 66
Speed | 0,5 / 0,8 |  |  |  |  |  | 
(m/s) | 1 |  |  |  |  |  | 
 | 1,6 / 1.75 |  |  |  |  |  | 
Entrances |  | 1 or |  |  |  |  | 
 |  | 2 (180°) |  |  |  |  | 
Low OVH / Low Pit |  |  |  |  |  |  | 
Car width |  |  | 1800 ÷ 2700 |  |  |  | 
Car depth |  |  | 2400 ÷ 3800 |  |  |  | 
Car height |  |  | 2200 ÷ 2700 |  |  |  | 
WTW (min) |  |  | 2670 (On Landing), 2795 (in Hoistway) |  |  |  | 
HW (min) |  |  | 2970 |  |  |  | 
 |  |  |  | Standard |  | No scope | 

## Slide 3
Key parameters
DOOR RANGE
CLD3
6 panels central
VARIABLE CAR DIMENSIONS
MACHINE LOCATION
Gen2 Robusta ED
9 m2
4,32 m2
CW variable
CD variable
Variable car dimensions
in 50mm steps
CLD2
4 panel central

## Slide 4
+
+
+
A better ride quality
10 milli-g horizontal vibration and 53dB(A) in car
Robustness
All the mechanical efforts go to a full robust car frame.
Roping 4:1
This allows to have high duties with smaller components (machine, drive etc.)
Belts
4:1 Under-slung
platform
Roping 4:1